## Slide 1
Indoor 3D Reconstruction from Laser Scanner Data
Smart Indoor Models in 3D (SIMs3D)
Shayan Nikoohemat
November 2018
Promoter: Prof. Dr. Ir. George Vosselman

## Slide 2
Indoor 3D Model Reconstruction to Support Disaster Management in Large Buildings
Smart Indoor Models in 3D (SIMs3D)

## Slide 3
Floor separation using the trajectory
Extracting the stair cases
Trying the algorithm on non-Manhattan World buildings (slanted wall, sloped ceiling)
Recovery of reflected points caused by reflective surfaces
Improving the space partitioning to 3D instead of 2.5D
… and of course write all of it in a paper 
List of improvements to the current algorithms:
Exploiting MLS Trajectory for Interpretation of Indoor laser Scanner Data

## Slide 4
Floors Separation:
Exploiting MLS Trajectory for Interpretation of Indoor laser Scanner Data
Use the z-histogram to find the picks as floors
Turner et al. (2015)
Oesau et al. (2014)

## Slide 5
Floors Separation:
Exploiting MLS Trajectory for Interpretation of Indoor laser Scanner Data
Use the z-histogram to find the picks as floors
Point clouds of
a-three-floor building
(Mezzanine Architecture)
Floor separation by
z-histogram

## Slide 6
Floors and Stairs Separation:
Exploiting MLS Trajectory for Interpretation of Indoor laser Scanner Data
The trajectory is used for floor separation.
The trajectory is segmented.
Associated points of each trajectory segment are selected as a space partition.
Segmented trajectory

## Slide 7
Structure Detection in non-Manhattan World Buildings: data from Mura et al (2016)
Towards Smart Indoor 3D Models Reconstructed from Point Clouds
Slanted Wall and non-horizontal ceiling detection based on different angle threshold
supported
supporter
Using the support relation between two almost-vertical wall candidates to detect slanted walls
Adjacency graph

## Slide 8
Towards Smart Indoor 3D Models Reconstructed from Point Clouds
Structure Detection in non-Manhattan World Buildings
Case 1, 2, 3 and 4 could be handled.
Case 5 can be problematic. Because the lower ceiling could be removed during the process.
Ceiling
Floor
Wall
Slanted Wall

## Slide 9
Removing reflected points
caused by glass surfaces:
Top view of the same area,
colored by time.
Top view. Reflected segments are green.
Top view of a room with reflected surfaces, yellow area.

## Slide 10
Recovering reflected points
caused by glass surfaces:
Top view of the same area
Top view: recovery process
Perspective view of a wall, glass and a reflected surface
Wall
Glass
Ghost Wall
Trajectory
(a)
(b)
(c)
(d)
(e)

## Slide 11
Towards Smart Indoor 3D Models Reconstructed from Point Clouds
Improving Space partitioning and navigable space:
Intersection of the space partitions with the trajectory
Removing partitions outside the building
Bottom view of partitions
and the trajectory
Perspective
view

## Slide 12
Towards Smart Indoor 3D Models Reconstructed from Point Clouds
Detecting Misclassified Walls:
Misclassified Walls
Detection
Correction

## Slide 13
Towards Smart Indoor 3D Models Reconstructed from Point Clouds
Tested MLS Devices:
ITC backpack
Zeb1
ZebRevo
NavVis M6

## Slide 15
Indoor 3D Model Reconstruction to Support Disaster Management in Large Buildings
WP3. Use Case
ITC backpack
Leica P20
iMS3D-Viametris
Scanning a complex multi-storey building
Compare the result with the BIM model

## Slide 16
Indoor 3D Model Reconstruction to Support Disaster Management in Large Buildings
WP3. Use Case
Flexible Space Subdivision (FSS) for accessibility
analysis (TUD method)
Making a final 3D model
second floor
BIM Model
Space partitions
first floor

## Slide 17
Indoor 3D Model Reconstruction to Support Disaster Management in Large Buildings
Smart Indoor Models in 3D (SIMs3D)
indoor
point clouds
Walls, floor, ceiling
Doors, openings
Free space
Navigable space
Clutter, obstacles
Integration of WP1 and WP2
WP1
(Geometry Extraction)
WP2
(Space Subdivision)

## Slide 18
Indoor 3D Model Reconstruction to Support Disaster Management in Large Buildings
Smart Indoor Models in 3D (SIMs3D)
WP2. 3D Models and Algorithms
User Centered Space Subdivision
Functional Space
The Flexible Space Subdivision (FSS) Framework
Object-Space, Functional-Space
and Remaining-Space (navigable space)
FSS of a BIM model

## Slide 19
Indoor 3D Model Reconstruction to Support Disaster Management in Large Buildings
Smart Indoor Models in 3D (SIMs3D)
Integration of WP1 and WP2
Motivation: using the real data to subdivide the space based on the permanent structures and dynamic objects (furniture) and agents
Ongoing Publication: Automation in Construction
(5 yrs impact factor 4.4)
Fixing undershooting problems
e.g. walls are not connected
Generate volumetric walls
Expected submission: End of January

## Slide 20
Indoor 3D Model Reconstruction to Support Disaster Management in Large Buildings
Smart Indoor Models in 3D (SIMs3D)
Conclusion:
The methods are tested successfully in different scenarios and various MLS devices.
The manual corrections are trivial for an expert
The accuracy of results is strongly dependent on the sensor accuracy and the noise.
Future Work:
Further work will be done for consistency check of the model during the integration process.
Possibility of doing an internship abroad.
Valorisation of the results in the future spin-off